## Slide 1: SRS Calibration
Michael Phipps, Bob Azmoun, Craig Woody

## Slide 2: SRS Calibrations: At least 4 issues to be mindful of and/or correct
Nonlinearity
Hybrid Saturation
FEC Saturation
Channel-to-Channel Differences

## Slide 3: 1) Nonlinearity calibration
MUX4 correction curve
Average Response Across All Channels Across all Input Values -> measures response nonlinearity
Nonlinearity as function of MUXGAIN and IMUXIN
Convert from electrons to corrected ADC
Conclusions:
Each MUXGAIN needs its own calibration curve
IMUXIN is just an additive constant -> nonlinearity is in the hybrid and independent of location in FEC range
Correction applied AFTER pedestal subtraction
FEC saturation

## Slide 4: Internal Pulser Pedestal Shift
Internal pulser causes a pedestal shift during pulse injection
To accurately measure the nonlinearity response the pedestal mean needs to be corrected for each time bin
This week: make corrected pedestal by using the average pedestal for all unused channels for each time bin (remember: internal pulser only injects 1 out of 8 channels)

## Slide 5: 2) Hybrid Saturation
SRS designed for silicon at CMS. GEM signal orders of magnitude larger -> primary charge saturates preamp inside the APV
MUXGAIN controls gain of multiplexer – located after the preamp/shaper, so cannot avoid saturation problem by changing MUXGAIN alone
Decreasing GEM gain to avoid saturation takes you below 10 mV discriminator threshold
Serious problem for wide readout strips (chevrons) or large drift detectors.
Time bin centroid measurements can help minimize by using many unsaturated samples
Clipping

## Slide 6: 3) FEC Saturation
Dynamic range between ~400 - 3200 ADC
Since largest MUX5 signal is ~2700 ADC, MUX5 should be avoided with GEMs
MUX3 and MUX4 pedestals have to be carefully aligned within the FECs dynamic range (modify the IMUXIN of the preamp)
Upper limit:
3200 ADC
Lower limit:
400 ADC
Pedestal above threshold
FEC Saturation

## Slide 7: 4) Channel-to-channel calibration
APV Internal Pulser
Internal Pulser
Mux 2
Internal Pulser
Mux 4
Channel dependent non-linearity curves
Signal response per channel

## Slide 8: MUXGAIN: *Resistors for Mux3 and 4 appear to be switched in all APVs (ie Mux 4 is nominal Mux)
MUX GAIN | Approximate Hybrid Range (Pedestal-subtracted ADC) | Multiplexer Gain (mA/mip)
1 | 1250 | 0.6
2 | 1700 | 0.8
3 | 2500 | 1.2
4 | 2100 (~11 bit) | 1.0
5 | 2900 | 1.4
MUXGAIN 1
MUXGAIN 2
MUXGAIN 3
MUXGAIN 4
MUXGAIN 5

## Slide 9: Signal to Noise of MUXGAIN Process
Crude measurement made from secondary peak using 2nd Fe55 peak (nonsaturated/linear)
Signal taken as mean of Gaussian across all channels
Ped RMS taken as RMS of same channel in all four MUX values (same source/same position/measurements taken sequentially)
Suggests that MUX3 (which is really MUX4) has best S/N
Makes sense since Multiplexer gain comes before noise incurred from HDMI cables and FEC electronics

## Slide 10: Operating conditions moving forward
MUXGAIN: 3 (which is actually MUX 4 -- highest MUX that doesn’t saturate the FEC – best S/N )
IMUXIN: 0x56
Hybrid saturation: Use time bin centroid routines whenever possible
Begin testing VMII chip to replace APV. Explore other readout systems